City of Havre de Grace                                                                          Department of Public Works                                                                               711 Pennington Avenue  •  Havre de Grace, MD 21078                                             Phone: 410-939-1800 ext. 1130  •   Fax: 410-939-7527

Road and Storm Drain

Plans Review Checklist

Project Name: _____________________________________________________________________

Tax Map __________  Parcel ___________  Acreage _______  Plat __________  ADC Map & Grid _____________

Owner’s Name:_____________________________________________________________________

Contract Purchaser’s Name: __________________________________________________________

______________________________________      ___________________________      _____________    _____________

Address                                                              City/Town                                      State                   Zip Code

Engineer/Surveyor: _________________________________________________________________

For additional contact: ______________________________________________________________

Name: ____________________________________________________________________________

The following is a list of the minimum requirements for review and approval of Roads and Storm Drains plans by the Department of Public Works.  Plans not meeting these minimum requirements will be deemed incomplete and returned to the Engineer.  Please complete and submit the checklist with three (3) paper copies with computations for review.  Road Plans shall be designed in accordance with the Harford County Road Code and Standard Specifications.

Upon final approval, the Owner/Engineer shall submit five (5) signed and sealed paper copies and one (1) set of mylars for signature along with two (2) sets of signed and sealed computations.  Upon signature of the plans by all parties, the engineer shall submit a pdf-file of plans and computations to the city of Havre de Grace.

CO/NA

__/__ 1. Road and Storm Drain Checklist

__/__ 2. Plans Sheets Standard thirty-six inch by twenty-four inch (36”x24”) size.

3. Title Sheet

__/__   a.  Location Map drawn to scale (1’ = 600 feet)  Map to indicate Tax map and Parcel Number,

bench marks and existing and proposed roads.

__/__   b.  City General Notes

__/__   c.  Owner/Developer and Engineer Certifications

__/__   d.  Geotechnical Certification and As-built Certification Blocks

4. Road Plan View

__/__    a.  Plan to scale of 1”=50’, 1”=40’, 1”=30’, or 1”=20’ with North arrow oriented to top of

page.

__/__    b.  Street names

__/__    c.  Right-of-way, Pavement and Easement widths, both existing and proposed clearly

defined.

__/__    d.  Bearing, distance, stationing of roadway centerlines, P.C.’s and P.T.’s and Roadway

Centerline P.I.’s

__/__    e.  Horizontal curve Information: Angle of Intersection, Center Line Radius, Tangent Length,

Length of Curve, Chord Bearing, and Chord Length.

__/__    f.   Stationing along centerline in even fifty foot sections

__/__    g.  Points of intersection of curb lines; Indicated by small linked crosses, and shall be

identified as N.E., N.W., S.W., or S.E.

__/__    h.  Existing and proposed Storm Drain clearly shown and labeled.

__/__     i.  Stations of P.C.’s and P.T.’s of curbs as well 25 foot stationing of curbs on circular

portions of cul de sacs and/or residential Intermediate turnarounds

__/__    j.   A minimum of three (3) NAD83m x,y coordinates at 250 feet intervals or (3) NAD 83 m

x,y coordinates ± 9 meters

__/__   k.   Bench Mark reference, Description and Elevation

__/__    l.   Show future roadway 200’ beyond Limit of Work

5. Profiles

__/__    a.  Profiles drawn horizontal scale 1” = 50’ and vertical scale 1” = 5’

__/__    b.  Existing grades at centerline of road and right and left of right of way limits

__/__    c.  Profile Grade Line: centerline of road or top of curb

__/__    d.  Existing and proposed elevations at 50’ intervals, 25’ intervals for vertical curves

__/__    e.  Label Elevations and stations for P.V.’s, P.V.R.C.’s, P.V.T.’s and P.V.I.’s

__/__    f.   Stopping Sight Distance

__/__    g.  Label, elevations and stations of sumps and crests along vertical curves

__/__    h.  Extended profile 200 feet beyond limits of work

__/__    i.  Horizontal Intersection Stations Identified

__/__    j.  Linear Profile of cul de sac and/or intermediate turnaround with existing and proposed

elevations at 25’ intervals.

*THE FOLLOWING NOTE SHALL BE ON THE PROFILE SHEET IN AREAS OF FILL.

Fill Material is to be controlled and compacted as certified by an approved Soils Engineer.  Fill Material is to be placed in no less than 4” and no greater than 8” lifts and rolled to 95 percent compaction within the top one (1) foot and 92 percent compaction elsewhere within Road right-of-way.

__/__  6. Storm Drains – Attached Hydraulic gradient & Head loss spread computations signed

and Sealed.

__/__    a. Scale

__/__    b. Crossing with existing and proposed utilities

__/__    c.  Pipe size (minimum 15”) Tupe (ACCMP, HDPE, CAP or class IV RCCP within the Road right

of way), Slope, Q₂₅  (cfs), Velocity (FPS), HGL-25 year storm plotted, Proposed and

existing grades, inverts, structures clearly labeled to match plan view

__/__    d.  Cross culverts designed on 25 year storm, show 2, 10 and 100 year Flood Elevation, Class

1 Rip Rap upstream, Class I & II Rip Rap with toe wall downstream per design calculations

__/__    e.  Outfall protection at all end walls/headwalls into existing systems

__/__    f.   Structure Schedule: Providing structure standards, top of grate/cover, invert elevations,

Comments

__/__    g.  Drainage area map (North arrow, scale, existing and future system)

__/__    h.  If open section roads are proposed, provide driveway, culvert computations and ditch

computations (Flow Tabulation Form). Refer to SHA 61.1-405.0 for maximum ditch

velocities permitted.)

7. Construction Details

__/__    a.  Curb details

__/__    b.  Pavement sections

__/__    c.   Inlet details